## Slide 1
An Equity-driven Approach for School Zone Safety to Inform Safe Routes to School (SRTS) Programs
Major Updates: Crash Analysis and Education Program
Mouyid Islam, PhD
Shuchi Deb, PhD
Monday, January 10, 2022
School Transportation, Convention center

## Slide 2
Rational – Research Motivation
Demo-
graphics
Actions and Locations
Vehicle Type and Maneuvers
Roadway Attributes
Education Program
Equity
5-11
12-14
15-19
School-age children account for nearly one-fifth of the total pedestrian fatalities. (Dangerous by Design, 2019)
Over 52% school-age pedestrians, killed in school transportation-related crashes, belong to the age group of 5-10 years. (NHTSA, 2020)

## Slide 3
Safety Analysis
(DFW & TB)
Engineering
Enforcement
Emergency Medical Services
Education
Study Approach

## Slide 4
Spatial Distribution of Pedestrian and Pedalcyclist Crashes in Tampa Bay Area in Florida
nearby the Elementary, Middle, and High Schools (2015-19)
Crash Data:
Data Source: CAR
Analysis Period: 2015-19
Study Area: Tampa Bay
(Hillsborough, Pasco, Pinellas)
Analysis Focus: Injury Severity (KABCO)
Severe = KA
Moderate = B
Minor = CO
N = 778
Chart: Florida Income ($)
| 8077 - 27830 | 27831 - 55660 | 55661 - 83490 | 83491 - 111330 | 111331 - 166980 | 166980+
Severe | 12 | 55 | 10 | 8 | 4 | 1
Moderate | 53 | 165 | 74 | 23 | 19 | 1
Minor | 47 | 173 | 84 | 19 | 8 | 1
Study Approach

## Slide 5
Chart: Age Distribution of Pedestrians/Pedalcyclists-involved Crashes within 0.5-mi of School Zone (Elementary, Middle, and High School) by Injury Severity in Tampa Bay (2015-19)
| 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19
Severe | 0 | 2 | 2 | 1 | 2 | 2 | 1 | 4 | 8 | 5 | 14 | 11 | 14 | 13 | 13
Moderate | 5 | 13 | 8 | 9 | 9 | 15 | 13 | 25 | 27 | 30 | 48 | 42 | 35 | 36 | 30
Minor | 6 | 6 | 8 | 11 | 9 | 16 | 19 | 27 | 14 | 41 | 46 | 43 | 27 | 37 | 31
Chart: Age Distribution of Drivers involved in Crashes within 0.5-mi of Schools (Elementary, Middle, and High Schools) by Injury Severity in Tampa Bay (2015-19)
| 16-29 | 30-49 | 50-65 | 65+
Severe Injury | 23 | 31 | 20 | 7
Moderate Injury | 71 | 107 | 74 | 34
Minor Injury | 60 | 111 | 61 | 33
Safety Analysis

## Slide 6
Chart: Crashes involving Pedestrians/Pedalcyclists' Actions Prior to Crashes within 0.5-mi of Schools (Elementary, Middle, and High Schools) by Injury Severity in Tampa Bay (2015-19)
| Crossing Roadway | Walking/cycling on Sidewalk | Walking with Traffic | In roadway | Going/from School | Walking Against Traffic | Adjacent to roadway
Severe Injury | 62 | 9 | 9 | 3 | 2 | 1 | 1
Moderate Injury | 223 | 39 | 22 | 18 | 8 | 12 | 4
Minor Injury | 215 | 49 | 24 | 15 | 14 | 7 | 1
Chart: Crashes involving Pedestrians/Pedalcyclists' Location at the time of Crash within 0.5-mi of Schools (Elementary, Middle, and High Schools) by Injury Severity in Tampa Bay (2015-19)
| INTX - Marked Xwalk | Travel Lane | INTX - Unmarked Xwalk | INTX - other | Shoulder/Roadside | Sidewalk | Drivway Access
Severe Injury | 25 | 21 | 9 | 7 | 8 | 6 | 1
Moderate Injury | 110 | 74 | 47 | 22 | 20 | 19 | 20
Minor Injury | 111 | 49 | 64 | 25 | 18 | 19 | 13
Safety Analysis

## Slide 7
Chart: Crashes involving Pedestrians/Pedalcyclists by involved Vehicles within 0.5-mi of Schools (Elementary, Middle, and High Schools) by Injury Severity in Tampa Bay (2015-19)
| PC | SUV | PICKUP | VAN | LGHT TRCK
Severe Injury | 52 | 18 | 9 | 5 | 1
Moderate Injury | 179 | 59 | 40 | 12 | 7
Minor Injury | 179 | 60 | 38 | 10 | 3
Chart: Crashes involving Pedestrians/Pedalcyclists by Number of Lane of Roadway within 0.5-mi of Schools (Elementary, Middle, and High Schools) by Injury Severity in Tampa Bay (2015-19)
| 2-Lane | 4-Lane | 6+ Lane | 3-Lane
Severe Injury | 54 | 17 | 18 | 0
Moderate Injury | 210 | 57 | 30 | 13
Minor Injury | 222 | 34 | 22 | 17
Chart: Crashes involving Pedestrians/Pedalcyclists by Number of Lane and Traffic Way within 0.5-mi of Schools (Elementary, Middle, and High Schools) by Injury Severity in Tampa Bay (2015-19)
| 2-Lane | 4-Lane | 6+ Lane | 3-Lane
2-way Undivided | 431 | 33 | 8 | 13
2-way, Positive Barrier | 20 | 56 | 57 | 10
2-way, painted Median | 20 | 13 | 2
TWLTL | 6 | 5 | 2 | 2
Safety Analysis

## Slide 8
Chart: Crashes involving Pedestrians/Pedalcyclists for Trafficway Controls within 0.5-mi of Schools (Elementary, Middle, and High Schools) by Injury Severity in Tampa Bay (2015-19)
| No Controls | Traffic Signal | Stop Sign | School Zone Sign
Severe Injury | 54 | 27 | 5 | 1
Moderate Injury | 169 | 82 | 71 | 4
Minor Injury | 173 | 61 | 75 | 9
Chart: Crashes involving Pedestrians/Pedalcyclists for Speed Limit within 0.5-mi of Schools (Elementary, Middle, High Schools) by Injury Severity in Tampa Bay (2015-19)
| <25 | 30-45 | 45+
Severe Injury | 18 | 68 | 4
Moderate Injury | 123 | 204 | 1
Minor Injury | 136 | 174 | 4
Safety Analysis

## Slide 9
Factors | Crash by percentage | 
 | Most frequent | Most severe
Road-way type | Undivided Road DFW: 50.5% TB: 77.1% | Undivided Road DFW: 58.2% TB: 71.7%
Traffic control | No Control DFW: 41.8% TB: 56.7% | No Control DFW: 49.5% TB: 60.6%
Vehicle type | Passenger Vehicle DFW: 56.6% TB: 64.8% | Passenger Vehicle DFW: 55.8% TB: 64.5%
Speed limit | 30-45 mph DFW: 84.2% TB: 58.5% | 30-45 mph DFW: 83.0% TB: 71.4%
Weather | Clear DFW: 77.7% TB: 85.4% | Clear DFW: 73.2% TB: 87.1%
Chart: DFW
| No control | Traffic signal | Stop sign
Severe | 96 | 61 | 37
Modertae | 178 | 168 | 85
Minor | 195 | 166 | 136
Chart: TB
| No control | Traffic signal | Stop sign
Severe | 40 | 22 | 4
Modertae | 137 | 59 | 51
Minor | 130 | 41 | 57
Chart: DFW
| < 25 | 30-45 | 45 +
Severe | 23 | 543 | 88
Moderate | 93 | 807 | 50
Minor | 104 | 804 | 45
Chart: TB
| <25 | 30-45 | 45+
Severe | 17 | 50 | 3
Moderate | 98 | 152 | 0
Minor | 108 | 122 | 4
Chart: TB
| 2-Lane | 3-Lane | 4-Lane | 6+ Lane
Two-way, Undivided | 332 | 9 | 23 | 3
Divided with barrier | 16 | 10 | 38 | 45

Chart: DFW
| 4-Lane | 5-Lane | 6-Lane | 7+ Lane
Two-way, Undivided | 4 | 6 | 57 | 68
Divided with barrier | 33 | 2 | 105 | 0
Differences in Crashes analysis: Roadway attributes
Traffic Control: DFW vs TB
Speed Limit: DFW vs TB
Number of Lane: DFW vs TB

## Slide 10
Scenarios for the Dallas-based Training Module | 
1. Road-way type Undivided 2. Number of lanes 2 and 4 3. Traffic control No control Traffic signal 4. Speed limit (mph) 20 and 45 5. Traffic volume 25,000 to 50,000 vehicles/day | 6. Weather Clear 7. Pedestrian location Marked crosswalk Unmarked crosswalk Midblock 8. Pedestrian action Crossing Waiting to cross 9. Obstacles Parked car Bushes/trees School bus
Education Program Development: Scenarios (VR)

## Slide 11
Scene | Vehicle Speed (mph) | Crosswalk Position | Crosswalk Type | Traffic Control
“Start Game” | --- | --- | --- | ---
Level 1 | 20 | Intersection | Marked | Present
Level 2 | 20 | Midblock | Unmarked | Absent
Level 3 | 20 | Intersection | Unmarked | Present
Level 4 | 20 | Intersection | Unmarked | Absent
Level 5 | 45 | Intersection | Marked | Present
Level 6 | 45 | Midblock | Unmarked | Absent
Level 7 | 45 | Intersection | Unmarked | Present
Level 8 | 45 | Intersection | Unmarked | Absent
“Complete” | --- | --- | --- | ---
Education Program Development: Scenarios (VR)

## Slide 12
Step 1
  The player will enter the "Playground," a 30 ft. long free floor space in the lab.
  They will stand on a designated area to stand and start the game.
  They will wear the HMD and take the Right-Hand Controller.
  Step 2
    The player will discover them in a virtual room with a "Play Game" button in front.
    Pressing the "Play Game" button, they will be on the edge of a street facing a crosswalk.
Education Program Development: Training Procedure

## Slide 13
Step 3
  There are two white dots on the street: "Start Point," and "End Point". Player starts the game from the "Start Point.
  Player will observe the surrounding and attempt to cross the street to reach the “End Point”.
  Step 4
  At End Point, the player will turn around (180 degrees) and see a button called "Next Level" across the street.
Education Program Development: Training Procedure
Step 5
  The player will repeat Step 3 and Step 4 until they complete all levels.
  When the player completes all eight levels, they will see a virtual room with a "Complete" button in front.
  If the player presses the "Complete" button, the study will end for this player and will be ready for the next player to play.

## Slide 14
(a) Marked Crosswalk (b) Unmarked Crosswalk (c) Midblock Crossing
(d) Pedestrian push-button (e) Pedestrian lights
Education Program Development: VR(HMD) - Plan VIEW

## Slide 15
Conclusions (Recommendations: education)
Education Video

## Slide 16
Questions?
mislam@vtti.vt.edu
540-231-5022